## Slide 1: MySQL and SSD: Usage Patterns
MySQL Conference & Expo 2011
12-Apr-2011
Vadim Tkachenko
Co-founder, CTO, Percona Inc
Date, time, place:
Reporter:

## Slide 2
You can get up to 7x gain running MySQL on SSD
  Even 20x with some tricks
Notes: Percona Server is not only about performance, but we have bunch of features that makes everyday work easier

## Slide 3: In this talk
What is best setup of MySQL to get most benefit from SSD / Flash
Notes: Percona Server is not only about performance, but we have bunch of features that makes everyday work easier

## Slide 4: What’s inside
MySQL and SSD: basics
MySQL and SSD: advanced schemas

## Slide 5: Types of SSD
SATA
PCI-E
SAN

## Slide 6: Types of SSD
SATA
  200-500MB/sec
  Intel X25-M/E, OCZ, Unigen
PCI-E
  Over 1GB/sec, 70.000 req/sec, under 1ms response time
  Virident, FusionIO
SAN
  Violin memory

## Slide 7: What is this for MySQL ?
1GB/sec – 70,000 req/sec
  A lot, but MySQL can’t use that all

## Slide 8: MySQL basic usage
  Put all data ( ibdata1, ib_log, tables.ibd) on SSD
    5-7x difference
Chart: tpcc 1000W (100G data) /13G memory
| RAID | tachIOn
 | 3297.8333 | 23669.9333

## Slide 9: MySQL basic usage
  Boring, some recommendation:
    XFS, better with 4k blocks
      Mkfs.xfs -s size=4096
      Mount –o nobarrier
    Multiple threads
    Percona Server or InnoDB-plugin or MySQL 5.5
  Still uses about 5,000 req/sec, ~200MB/sec

## Slide 10: Can we do better ?
  Single threaded sequential stuff
    InnoDB transactional logs with fsyncs
    Binary logs
    Doublewrite buffer ( with whole ibdata)
  RAID with BBU good place for them
    Up to 45% improvement
Chart: NOTPM
| logs on RAID | logs on tachIOn
 | 30692.8 | 21224.8

## Slide 11: What is in Percona Server for it ?
  innodb_flush_neighbor_pages= ON | OFF
  innodb_log_block_size = 512 | 4096
  innodb_page_size = 4K | 8K | 16K
    Use carefully
  innodb_doublewrite_file
  Innodb_adaptive_checkpoint=keep_average
  innodb_log_file_size > 4GB

## Slide 12: What if ?
  Data is too large
    Or SSD too small

## Slide 13: Naive solution
  Most data on regular disks
  Put “hot” ibd files on SSD
    Symlinks from data directory

## Slide 14: Naive solution
  It works
  But pain to manage and till first “ALTER TABLE”
  Facebook has patch for it

## Slide 15: Advanced solution: caching
  Data stored on regular disks
    Caching data on SSD
  Flashcache
    Open source
    Developed and maintained by Facebook, deployed in production
  DirectCache
    Proprietary solution from FusionIO

## Slide 16: FlashCache
  Shows good results
  Stable work in production deployments
  Not much user friendly

## Slide 17: FlashCache details
  Write-through and write-back modes
  FIFO and LRU block management
  You need to compile kernel module by yourself
  The same choice for ibdata1/ib_logs location

## Slide 18: ZFS
  ZFS supports SSD caching mode
  Linux native port available

## Slide 19: Interesting trick
  For temporary tables on disks
  --tmpdir=/mnt/ssd

## Slide 20: Still not enough space?
  Several SSD / Flash cards in the server

## Slide 21: Combining cards
  SATA
    Choice good RAID controller, maybe challenge
  PCI-E
    Software RAID
      Usually comes as stripping ( RAID0 )
      Reliability ?
      Mirroring does not work really well

## Slide 22: What about promised 20x ?
Single MySQL instance is not able to utilize all IO provided by card

## Slide 23: Several instances
Solution obvious:
  Several instances

## Slide 24: Experiment
Dell PowerEdge R815
4 physical AMD CPUs / 48 cores
144GB of RAM
Virident tachIOn 200GB card
48 user connections

## Slide 25: Experiment
Dell PowerEdge R815
4 physical AMD CPUs / 48 cores
144GB of RAM
Virident tachIOn 200GB card
Tpcc-mysql workload
  48 user connections

## Slide 26: Results

## Slide 27: Results conclusions
With 120GB memory single instance result worse then with 26GB
  InnoDB contentions problems again
Two instances allows to improve 1.5x-6x

## Slide 28: Multi-instance
I do not like it
  Management complexity
  Good scripts solve it
2 instances seems reasonable
SAN-like Flash-arrays

## Slide 29: The end
Slides will be online. http://www.percona.com/about-us/presentations/
vadim@percona.com
Your questions ?
We are hiring!
Notes: If you are familiar with cache concepts, there two popular ways to handle writes, and FlashCache supports both of them: Write Through and Write Back.