## Slide 1: Profiling and Detecting Bottlenecks in Software
Bryan Call
OSCON 2011
Yahoo! Engineer and Apache Commiter

## Slide 2: Overview
Why profile your code?
Rules of thumb
Profiling pitfalls
Types of bottlenecks
Basic command line tools
What is a profiler?
Types of profilers
Profiling Examples
Ways to improve performance

## Slide 3: Why profile your code?
Better understanding of your application and architecture
Reduced hardware and maintenance costs
  Less hardware to setup and maintain
Learn how to be a better coder
Look smart

## Slide 4: Rule of thumb
80/20 rule
  80% of the runtime using only 20% of the code
  Some people say 90/10

## Slide 5: Profiling pitfalls
Pre-optimization, waist of time
  Optimizing the 80% of the code that only runs 20% of the time
  Don’t fully understand the architecture or workload
Over optimize code
  Can overcomplicate code

## Slide 6: Types of Bottlenecks
CPU
Disk
Network
Memory
Lock contention
External resources
  Databases, web service, etc..

## Slide 7: Basic Command-line Tools
top, htop (great for threaded apps)
vmstat, dstat
strace
time
Notes: Some utilities I use to track down what is the bottleneck for applications – I use dstat, htop, and strace a lot. I will use time for a quick test to see if how much system vs user time an application is using

## Slide 8: htop Example
4 core server

## Slide 9: htop Example
24 “core” – 12 core with hyper-threading

## Slide 10: dstat Example – CPU bottleneck
Apache Traffic Server – 470B objects in cache
Notes: Cpu is the bottleneck for apache traffic server in this example – network is about ¼ of the nic and hardly any disk io

## Slide 11: Understand Your Workload
Changing the workload can change the bottleneck

## Slide 12: dstat Example – Network bottleneck
Apache Traffic Server – 200KB object in cache
Notes: If your application looks similar to this it is pointless to optimize the code – 4% CPU used and 2% user – think about NIC bonding or 10gige

## Slide 13: dstat Example – Disk bottleneck
dd - /dev/zero to raid0 (two drives)
Notes: 2 things to note– disk writes are a bottleneck and we are using 7 to 9 times as much system time then user time – again pointless to optimize code if you are bottlenecked on hardware – think about a better raid, ssds, or compression before writing to disk

## Slide 14: dstat Example - syscall issue
Writes are too small and can’t max out the disk
Notes: 8x system over user and writes are down from ~175MB/sec
Story about boost logging – memory allocation & small writes even on separate writer thread
Story about interleaving small writes in the kernel

## Slide 15: strace Example
Effects performance ~100MB/sec to 1.1MB/sec
Notes: Performance change is exaggerated because of the number of system calls

## Slide 16: What is a Profiler?
Dynamic program analysis
Shows
  Frequency of functions called
  Usage of lines in code
  Duration of function calls

## Slide 17: Types of Profilers
Statistical
  Examples: oprofile, google profiler
  Good for interactive systems with lots of code
  Doesn't slow down the application much (1% to 8%)
  Fixed cost
    Doesn't take up more CPU as the number of function calls per second increases
Notes: ----- Meeting Notes (7/25/11 21:01) -----
Doesn't effect user experience

## Slide 18: Types of Profilers
Instrumenting
  Examples: valgrind's callgrind, gprof
  More detail (time for each function call)
  Can make programs much slower
  Good for non-interactive systems

## Slide 19: Oprofile
Requires kernel driver, need root access
System wide profiling, profiles everything running
Application doesn’t know about the profiler
Scripts to convert output for kcachegrind

## Slide 20: Oprofile Example
Profiling ab (Apache Bench)
30K rps with profiler, 32K rps without

## Slide 21: Oprofile Example

## Slide 22: Oprofile Example

## Slide 23: Oprofile Example
Showing everything that was running

## Slide 24: Google profiler
All in userland
Profiles specific applications, not system wide
Command-line LD_PRELOAD support
Support to build it into your application
Has graphing built in

## Slide 25: Google Profiler Example
Profiling ab (Apache Bench)
30K rps with profiler, 32K rps without
Notes: Really didn’t slow down ab much

## Slide 26: Google Profiler Example

## Slide 27: Google Profiler Example
Making a diagram of the profile

## Slide 28: Google Profiler Example

## Slide 29: Google Profiler Example

## Slide 30: Vagrind’s callgrind
All in userland
Requires no code changes
Really slows down your application
Lots of detail since it is not sampling

## Slide 31: callgrind Example
Running callgrind on ab (Apache Bench)
1.6K rps with profiler, 32K rps without - 95% slower

## Slide 32: callgrind Example

## Slide 33: callgrind Example - kcachegrind

## Slide 34: Recap
Understand your workload
Find your bottleneck
Profile

## Slide 35: Ways to Improve Performance
Caching
  Don't do the same work twice
Choose the correct algorithms and data structures
  dqueue vs list, hash vs trees, locks vs read/write locks, bloom filter
Memory allocation
  Reuse memory, stack vs heap, tcmalloc
Make fewer system calls
  Larger writes and reads
Faster hardware
  Bonded NICs, SSDs or RAID, CPU more cores

## Slide 36: References
Email: bcall@apache.org
How to profile ATS
  https://cwiki.apache.org/TS/profiling.html

## Slide 37: Links to Software
dstat
  http://dag.wieers.com/home-made/dstat/
htop
  http://htop.sourceforge.net/
oprofile
  http://oprofile.sourceforge.net/news/
google profiler (part of the prof tools)
  http://code.google.com/p/google-perftools/
callgrind
  http://valgrind.org/docs/manual/cl-manual.html
kcachegrind
  http://kcachegrind.sourceforge.net/html/Home.html

## Slide 38: Appendix
setup httpd/ab:
cd ~/tmp/
wget http://mirror.candidhosting.com/pub/apache//httpd/httpd-2.2.19.tar.bz2
tar xf httpd-2.2.19.tar.bz2
cd httpd-2.2.19
./configure
gmake -j 8
cd support

## Slide 39: Appendix
oprofile commands:
# at the start - only need to this once after reboot - because of watchdog timers
sudo opcontrol --deinit
sudo bash -c 'echo 0 > /proc/sys/kernel/nmi_watchdog'
sudo opcontrol --no-vmlinux
sudo opcontrol --start-daemon
sudo opcontrol --reset
sudo opcontrol --status
# in another terminal run ab - needs to run for 60 seconds, increase -n if need be
.libs/ab -k -n 2000000 -c 100 -X homer.bryancall.com:8080 http://l.yimg.com/a/i/ww/met/mod/ybang_22_111908.gif
sudo opcontrol -s; sleep 60; sudo opcontrol -t
sudo opcontrol --dump
sudo opreport --symbols .libs/ab 2>/dev/null
sudo opreport -cg 2>/dev/null | head -50

## Slide 40: Appendix
google profiler commands:
export CPUPROFILE=/tmp/mybin.prof
LD_PRELOAD="/usr/lib64/libprofiler.so" .libs/ab -k -n 2000000 -c 100 -X homer.bryancall.com:8080 http://l.yimg.com/a/i/ww/met/mod/ybang_22_111908.gif
pprof --text .libs/ab /tmp/mybin.prof | head
pprof --pdf .libs/ab /tmp/mybin.prof > ~/Desktop/ab.pdf

## Slide 41: Appendix
callgrind commands:
rm -f callgrind.out.* # clean up anything there
valgrind --tool=callgrind .libs/ab -k -n 100000 -c 100 -X homer.bryancall.com:8080 http://l.yimg.com/a/i/ww/met/mod/ybang_22_111908.gif
callgrind_annotate --tree=caller callgrind.out.*
kcachegrind callgrind.out.*

## Slide 42: Notes
Had problems with --separate=lib or --separate=thread not changing output on Fedora Core 15