## Slide 1: Design and Analysis of the World’s Most Advanced Microprocessors Jupyter and our transformational journey
Kerim Kalafala (i) and Nicholai L’Esperance (ii) on behalf of IBM Systems
(i) Member IBM Academy of Technology, Master Inventor, STSM
(ii) Processor Diagnostics Team

## Slide 2: Agenda
IBM Systems
Electronic Design Automation Use Case for Jupyter
Product Engineering Use Case for Jupyter
Reflections on Jupyter (so far…)

## Slide 3: System Overview
System Performance
Peak performance of 200 petaflops for modeling & simulation
Peak of 3.3 ExaOps for data analytics and artificial intelligence
Each node has
  2 IBM POWER9 processors
  6 NVIDIA Tesla V100 GPUs
  608 GB of fast memory
  1.6 TB of NVMe memory
The system includes
  4608 nodes
  Dual-rail Mellanox EDR InfiniBand network
  250 PB IBM Spectrum Scale file system transferring data at 2.5 TB/s
New 200-Petaflops System is World’s Most Powerful and World’s Smartest Supercomputer for Science

## Slide 4: IBM Power9 Processor
Up to 24 cores
  Summit’s P9s have 22 cores for yield optimization on first processors
PCI-Express 4.0
  Twice as fast as PCIe 3.0
NVLink 2.0
  Coherent, high-bandwidth links to GPUs
14nm FinFET SOI technology
  8 billion transistors
Cache
  L1I: 32 KiB per core, 8-way set associative
  L1D: 32KiB per core, 8-way
  L2: 258 KiB per core
  L3: 120 MiB eDRAM, 20-way

## Slide 5
IBM’s Flagship Mainframe
Z- “Zero Downtime”
Hardware accelerated, pervasive encryption.
“The new IBM z14 single frame model can process 850 million encrypted transactions per day in the space of two floor tiles”

## Slide 6: Agenda
IBM Systems
Electronic Design Automation Use Case for Jupyter
Product Engineering Use Case for Jupyter
Reflections on Jupyter (so far…)

## Slide 7: Electronic Design Automation (EDA)
Millions of lines of logic design (VHDL)
Detailed circuit implementation ready for manufacture
EDA
Logic Design
Verification
Compile in to circuits

## Slide 8
Processor Design Flow
I work here !
Will our design operate at the right frequency ?
Will our chips overheat ?
Are there transient/noise issues that could cause problems ?

## Slide 9: A day in the life of an analysis engineer
6PM the day before..
  Latest version of a design is available
  Kick off analysis tools
  Minutes  Several hours runtime
8AM the next day
  My analysis runs have completed
  100MB – 1GB report data available
8AM-onwards
  What needs to be fixed to improve my timing, power, noise ?
  Who needs to fix this ?
  Assign tasks
  Hours  Days of work
The faster engineers can complete the above, the more design iterations we can perform, which leads to shorter time to market, better performance, lower power, etc.

## Slide 10: Vision for a smarter chip design driven by a smarter EDA
Provide EDA Data as a Service on the Cloud
  Any engineer should have access to data relevant to do their job at any time on the web
  No more chasing data, parsing reports
Provide EDA Analytics as a Service
  API interface for power-users
  Web-interface for common tasks
Learn & evolve through designer interaction
  What are the most popular queries ?
  How are particular classes of design problems most frequently addressed ?
  How has this design progressed over time ?

## Slide 11
Overall Architecture
Traditional tool environment which produces data
New DAaaS environment which analyzes and serves data
Chart courtesy IBM ExtremeBlue

## Slide 12: Jupyter Notebooks for Prototyping (Python)
1. Tune complex database query
2. Collect output
3. Perform analysis using in-core DF
4. Examine results
Extremely fast iteration

## Slide 13
DAaaS Built with Jupyter
Publish ”verified” code in to DaaS framework

## Slide 14
GitHub Enterprise repo
Verified notebooks
Raw python
(Future)
(Now)
Enable more “power-users”
Future: JupyterHub

## Slide 15: Agenda
IBM Systems
Electronic Design Automation Use Case for Jupyter
Product Engineering Use Case for Jupyter
Reflections on Jupyter (so far…)

## Slide 16: Product Engineering
From product inception to market.
  Design
  Develop
  Test
  Analyze
Design Develop Test Analyze
Nicholai works here!
Kerim works here!

## Slide 17: Building a Chip that Works
I work here !
Is there a pattern to these fails?
Why are parts X running faster than parts Y?
Is there a specific circuit that is causing these failures?

## Slide 18: Product Engineering: Diagnostics
Binary Test Data
001111010111101110100101111010100110100101010001001101010101001000010100001010101010110111010110101010100
Decode
Analyze
Simulate
Out of trillions, one.

## Slide 19: Diagnosing Processors in Jupyter
Rate of Failure by Pin
Why Python + Jupyter?
  Python’s versatility allows integrating disparate data sources into a single analysis.
  Jupyter workflows give engineers easy, inline sanity checks.
  Visualization is vital to narrowing the search for systematics.
  Quick resolution saves massive resources—real dollars as well as engineering hours.
Test Data
Circuit Model
Physical Data
Configuration Data

## Slide 20: Diagnosing Processors in Jupyter
Every problem is different.
  Clever plotting and tabulation to help identify root cause.
  All aspects of the data must be examined:
    Logical: circuit names, circuit types
    Physical: circuit layout, circuit structure
    Geographical: wafer location, die location
    Temporal: manufacturing date
    Logistical: manufacturing events, test version
Count of Devices Failing Test X
Heatmap Of Failing Circuits
1) Gather data
3) Plot, tabulate
4) Check for outliers,
trends
2) Pivot, summarize,
transform

## Slide 21: Agenda
IBM Systems
Electronic Design Automation Use Case for Jupyter
Product Engineering Use Case for Jupyter
Reflections on Jupyter (so far…)

## Slide 22: Making Jupyter ”Enterprise” Ready
JupyterHub is the next step in an enterprise environment; “roadbumps” have slowed widespread adoption.
Setup Complexity
  No good solution without root access (required for process forking).
  Requires fairly in-depth knowledge of sub-components to implement.
    Documentation is essential—analysts are not implementing JupyterHub, sys-admins are (in an enterprise environment).
    “How to Setup” decision tree

## Slide 23: Making Jupyter ”Enterprise” Ready
Resource control
  Notebook memory usage monitoring, quota.
    Useful even on the single user level.
  External solutions/containers leave users blind to resource usage.

## Slide 24: JupyterCon Revelations
JupyterHub projects are very exciting.
The Littlest JupyterHub is a promising stepping stone in enterprise.

## Slide 25: Questions?